## Slide 1
MESA STEERING COMMITTEE MEETING 2019
NORTHWESTERN UNIVERSITY FEINBERG SCHOOL OF MEDICINE
MESA Early Heart Failure Study
Echo Core Lab Report
Sanjiv J. Shah, MD, FAHA, FACC, FASE
Stone Professor of Medicine
Director, T1 Center for Cardiovascular Therapeutics
Director, Northwestern HFpEF Program
Division of Cardiology, Department of Medicine
Northwestern University Feinberg School of Medicine
sanjiv.shah@northwestern.edu  http://www.hfpef.org  Twitter: @HFpEF

## Slide 2
MESA Exam 6 echo analysis: progress
Phase 1 (complete May 2019):
  Chamber quantification (LV, LA, RV, RA):
  Tissue Doppler, Doppler, diastology, hemodynamics:
  Qualitative valve assessment:
  LV longitudinal strain, LA strain (A4c view only):
  Legs up analysis:
Phase 2 (complete Q4 2019):
  Completed strain analysis (LV, RV, LA, RA, bullseye), regional strain analysis
  Echo pulse wave velocity
Phase 3 (complete Q4 2020):
  Pressure-stress, pressure-strain analyses
  Deep learning / computer vision quantitation of echocardiograms
  Automated echo analysis, pattern detection

## Slide 3
MESA Exam 6 echo analysis: progress
Phase 1 (complete May 2019): Total N=3035 echos
  Chamber quantification (LV, LA, RV, RA): 92% complete (EF 100% complete)
  Tissue Doppler, Doppler, diastology, hemodynamics: 100% complete
  Qualitative valve assessment: 100% complete
  LV longitudinal strain, LA strain (A4c view only): 100% complete
  Legs up analysis: 100% complete
Phase 2 (complete Q4 2019):
  Completed strain analysis (LV, RV, LA, RA, bullseye), regional strain analysis
  Echo pulse wave velocity
Phase 3 (complete Q4 2020):
  Pressure-stress, pressure-strain analyses
  Deep learning / computer vision quantitation of echocardiograms
  Automated echo analysis, pattern detection

## Slide 4
MESA guide to echo phenotypes
Domain | Parameters
Cardiac structure | LV dimensions/volumes, LV mass, relative wall thickness, LA volume, RV areas, RA area
LV systolic function | LV ejection fraction, LV longitudinal strain
LV diastolic function | LV E/A ratio, E deceleration time, early diastolic (e’) velocity, LV early diastolic strain rate, E/e’ ratio
LA function | LA reservoir strain, LA booster strain, LA conduit strain
RV systolic function | RV fractional area change, RV s’ velocity, TAPSE
RV diastolic function | RV E/A ratio, E deceleration time, RV E/e’ ratio
Hemodynamics | Stroke volume, cardiac output, RA pressure, PA systolic pressure, estimated pulmonary capillary wedge pressure

## Slide 5
MESA guide to echo phenotypes
Domain | Parameters
Cardiac structure | LV dimensions/volumes, LV mass, relative wall thickness, LA volume, RV areas, RA area
LV systolic function | LV ejection fraction, LV longitudinal strain
LV diastolic function | LV E/A ratio, E deceleration time, early diastolic (e’) velocity, LV early diastolic strain rate, E/e’ ratio
LA function | LA reservoir strain, LA booster strain, LA conduit strain
RV systolic function | RV fractional area change, RV s’ velocity, TAPSE
RV diastolic function | RV E/A ratio, E deceleration time, RV E/e’ ratio
Hemodynamics | Stroke volume, cardiac output, RA pressure, PA systolic pressure, estimated pulmonary capillary wedge pressure

## Slide 6
Intra-observer variability (n=100)
Parameter | Mean ± SD | ICC (95% CI) | Mean bias (95% CI)
Septal wall thickness (cm) | 1.15±0.20 | 0.96 (0.94, 0.98) | 0.02 (0.01, 0.04)
LV end-diastolic dimension (cm) | 4.37±0.50 | 0.97 (0.95, 0.98) | -0.01 (-0.04, 0.03)
Posterior wall thickness (cm) | 0.96±0.13 | 0.83 (0.73, 0.89) | 0.02 (0.00, 0.04)
LV end-systolic dimension (cm) | 2.85±0.41 | 0.97 (0.96, 0.98) | 0.02 (-0.01, 0.04)
LA volume (ml) | 55.9±17.2 | 0.97 (0.95, 0.98) | -0.48 (-1.64, 0.67)
LV end-diastolic volume (ml) | 80.2±19.9 | 0.98 (0.96, 0.99) | 0.72 (-0.48, 1.91)
LV end-systolic volume (ml) | 29.7±10.9 | 0.98 (0.96, 0.99) | -0.30 (-0.93, 0.33)
LA strain peak positive (A4c, %) | 12.2±5.2 | 0.96 (0.94, 0.98) | 0.30 (-0.07, 0.67)
LA strain peak negative (A4c, %) | 13.2±3.2 | 0.91 (0.85, 0.94) | -0.12 (-0.45, 0.20)
Legs up LA strain peak+ (A4c, %) | 15.1±4.8 | 0.94 (0.90, 0.96) | 0.16 (-0.29, 0.62)
Legs up LA strain peak- (A4c, %) | 12.1±3.5 | 0.90 (0.84, 0.94) | -0.10 (-0.52, 0.32)
LV longitudinal strain (A4c, %) | 20.8±3.1 | 0.93 (0.89, 0.96) | 0.06 (-0.22, 0.34)
LV early diastolic strain rate (A4c, 1/s) | 1.2±0.4 | 0.94 (0.90, 0.96) | 0.02 (-0.02, 0.06)
Early mitral inflow (E) velocity (cm/s) | 78.6±18.8 | 0.98 (0.96, 0.99) | 0.87 (-0.43, 2.17)
Late mitral inflow (A) velocity (cm/s) | 83.9±21.1 | 0.97 (0.94, 0.99) | 0.30 (-1.24, 1.84)
Septal e’ velocity (cm/s) | 7.3±1.8 | 0.91 (0.82, 0.95) | 0.07 (-0.16, 0.31)
Lateral e’ velocity (cm/s) | 9.0±2.1 | 0.90 (0.81, 0.95) | -0.24 (-0.58, 0.10)

## Slide 7
Inter-observer variability (n=100)
Parameter | Mean ± SD | ICC (95% CI) | Mean bias (95% CI)
Septal wall thickness (cm) | 1.15±0.20 | 0.80 (0.67, 0.89) | 0.01 (-0.01, 0.03)
LV end-diastolic dimension (cm) | 4.37±0.50 | 0.91 (0.85, 0.95) | -0.05 (-0.09, -0.02)
Posterior wall thickness (cm) | 0.96±0.13 | 0.81 (0.70, 0.89) | -0.02 (-0.04, 0.01)
LV end-systolic dimension (cm) | 2.85±0.41 | 0.83 (0.72, 0.90) | 0.06 (0.01, 0.11)
LA volume (ml) | 55.9±17.2 | 0.95 (0.91, 0.97) | -0.23 (-1.52, 1.06)
LV end-diastolic volume (ml) | 80.2±19.9 | 0.89 (0.81, 0.94) | -4.73 (-6.21, -3.25)
LV end-systolic volume (ml) | 29.7±10.9 | 0.87 (0.78, 0.93) | -2.82 (-3.79, -1.85)
LA strain peak positive (A4c, %) | 12.2±5.2 | 0.89 (0.82, 0.94) | -1.30 (-1.93, -0.67)
LA strain peak negative (A4c, %) | 13.2±3.2 | 0.81 (0.70, 0.89) | -0.97 (-1.44, -0.50)
Legs up LA strain peak+ (A4c, %) | 15.1±4.8 | 0.73 (0.57, 0.85) | -0.38 (-1.11, 0.36)
Legs up LA strain peak- (A4c, %) | 12.1±3.5 | 0.65 (0.47, 0.80) | -0.70 (-1.19, -0.22)
LV longitudinal strain (A4c, %) | 20.8±3.1 | 0.82 (0.71, 0.90) | -0.69 (-1.08, -0.30)
LV early diastolic strain rate (A4c, 1/s) | 1.2±0.4 | 0.90 (0.83, 0.95) | -0.07 (-0.11, -0.02)
Early mitral inflow (E) velocity (cm/s) | 78.6±18.8 | 0.99 (0.98, 0.99) | -1.04 (-1.58, -0.49)
Late mitral inflow (A) velocity (cm/s) | 83.9±21.1 | 0.96 (0.94, 0.98) | -1.07 (-2.10, -0.05)
Septal e’ velocity (cm/s) | 7.3±1.8 | 0.94 (0.90, 0.96) | -0.03 (-0.16, 0.11)
Lateral e’ velocity (cm/s) | 9.0±2.1 | 0.95 (0.93, 0.97) | -0.18 (-0.30, -0.05)

## Slide 8
Inter-observer variability (n=100)
Parameter | Mean ± SD | ICC (95% CI) | Mean bias (95% CI)
Septal wall thickness (cm) | 1.15±0.20 | 0.80 (0.67, 0.89) | 0.01 (-0.01, 0.03)
LV end-diastolic dimension (cm) | 4.37±0.50 | 0.91 (0.85, 0.95) | -0.05 (-0.09, -0.02)
Posterior wall thickness (cm) | 0.96±0.13 | 0.81 (0.70, 0.89) | -0.02 (-0.04, 0.01)
LV end-systolic dimension (cm) | 2.85±0.41 | 0.83 (0.72, 0.90) | 0.06 (0.01, 0.11)
LA volume (ml) | 55.9±17.2 | 0.95 (0.91, 0.97) | -0.23 (-1.52, 1.06)
LV end-diastolic volume (ml) | 80.2±19.9 | 0.89 (0.81, 0.94) | -4.73 (-6.21, -3.25)
LV end-systolic volume (ml) | 29.7±10.9 | 0.87 (0.78, 0.93) | -2.82 (-3.79, -1.85)
LA strain peak positive (A4c, %) | 12.2±5.2 | 0.89 (0.82, 0.94) | -1.30 (-1.93, -0.67)
LA strain peak negative (A4c, %) | 13.2±3.2 | 0.81 (0.70, 0.89) | -0.97 (-1.44, -0.50)
Legs up LA strain peak+ (A4c, %) | 15.1±4.8 | 0.73 (0.57, 0.85) | -0.38 (-1.11, 0.36)
Legs up LA strain peak- (A4c, %) | 12.1±3.5 | 0.65 (0.47, 0.80) | -0.70 (-1.19, -0.22)
LV longitudinal strain (A4c, %) | 20.8±3.1 | 0.82 (0.71, 0.90) | -0.69 (-1.08, -0.30)
LV early diastolic strain rate (A4c, 1/s) | 1.2±0.4 | 0.90 (0.83, 0.95) | -0.07 (-0.11, -0.02)
Early mitral inflow (E) velocity (cm/s) | 78.6±18.8 | 0.99 (0.98, 0.99) | -1.04 (-1.58, -0.49)
Late mitral inflow (A) velocity (cm/s) | 83.9±21.1 | 0.96 (0.94, 0.98) | -1.07 (-2.10, -0.05)
Septal e’ velocity (cm/s) | 7.3±1.8 | 0.94 (0.90, 0.96) | -0.03 (-0.16, 0.11)
Lateral e’ velocity (cm/s) | 9.0±2.1 | 0.95 (0.93, 0.97) | -0.18 (-0.30, -0.05)

## Slide 9
Temporal drift (n=10, measured q6mo x 5)
Parameter | Mean ± SD | ICC (95% CI) | Beta-coefficient | P-value
Septal wall thickness (cm) | 1.25 ± 0.22 | 0.97 (0.92, 0.99) | 0.000 (-0.008, 0.007) | 0.92
Posterior wall thickness (cm) | 0.93 ± 0.11 | 0.70 (0.36, 0.90) | 0.000 (-0.004, 0.003) | 0.84
LV end-diastolic dimension (cm) | 3.90 ± 0.49 | 0.95 (0.87, 0.99) | -0.002 (-0.019, 0.014) | 0.79
LV end-systolic dimension (cm) | 2.57 ± 0.33 | 0.94 (0.83, 0.98) | 0.002 (-0.009, 0.014) | 0.66
LV end-diastolic volume (ml) | 63.3 ± 10.82 | 0.97 (0.90, 0.99) | -0.032 (-0.398, 0.334) | 0.86
LV end-systolic volume (ml) | 23.5 ± 5.59 | 0.95 (0.86, 0.99) | 0.007 (-0.183, 0.196) | 0.94
LV ejection fraction (%) | 63.4 ± 3.47 | 0.77 (0.48, 0.93) | -0.007 (-0.124, 0.111) | 0.91
LA volume (ml) | 40.5 ± 9.25 | 0.92 (0.79, 0.98) | 0.102 (-0.210, 0.413) | 0.52
Mitral E velocity (cm/s) | 67.5 ± 15.24 | 0.97 (0.92, 0.99) | 0.080 (-0.435, 0.595) | 0.76
Mitral A velocity (cm/s) | 81.6 ± 18.35 | 0.98 (0.95, 1.00) | -0.020 (-0.641, 0.602) | 0.95
Septal e’ velocity (cm/s) | 7.3 ± 2.40 | 0.87 (0.67, 0.96) | -0.019 (-0.100, 0.063) | 0.65
Lateral e’ velocity (cm/s) | 9.3 ± 2.00 | 0.98 (0.95, 1.00) | -0.010 (-0.078, 0.058) | 0.77
LA strain peak positive (A4c, %) | 15.2 ± 2.64 | 0.69 (0.36, 0.90) | -0.016 (-0.106, 0.073) | 0.72
LA strain peak negative (A4c, %) | 8.8 ± 3.08 | 0.88 (0.70, 0.97) | -0.054 (-0.157, 0.050) | 0.30

## Slide 10
MESA Early HF definition
Prevalence estimates based on hospitalized HFpEF mainly
Sometimes defined by outpatient HFpEF dx.
Many cases of early HFpEF likely missed
HFpEF in US: 3 million vs. 6+ million?

## Slide 11
Types of HFpEF: clinical presentation
ENVIRONMENT, DIET
COMORBIDITIES
GENETIC SUSCEPTIBILITY
VULNERABLE HEART,
VULNERABLE PATIENT
HFpEF
Type 1:
EXERCISE-INDUCED
LA PRESSURE
Type 2:
VOLUME
OVERLOAD
Type 3:
PULMONARY HTN,
RV FAILURE
Shah SJ. JACC 2013

## Slide 12
Types of HFpEF: clinical presentation
ENVIRONMENT, DIET
COMORBIDITIES
GENETIC SUSCEPTIBILITY
VULNERABLE HEART,
VULNERABLE PATIENT
HFpEF
Type 1:
EXERCISE-INDUCED
LA PRESSURE
Type 2:
VOLUME
OVERLOAD
Type 3:
PULMONARY HTN,
RV FAILURE
Shah SJ. JACC 2013

## Slide 13
Diagnosis of HFpEF: H2FPEF score
Dyspnea on exertion, normal EF
HFpEF vs. non-cardiac dyspnea?
Intermediate pre-test probability
Nomogram below table for probability of HFpEF based on score:
A score of 4 or higher = 70% probability of HFpEF
A score of 5 or higher = >80% probability of HFpEF
A score of 7 or higher = >95% probability of HFpEF
Reddy YN…Borlaug BA. Circulation 2018

## Slide 14
Diagnosis of HFpEF: ESC HFA-PEFF score
Septal e’ < 7,
Lateral e’ < 10,
or
E/e’ (avg) ≥ 15
LAVI > 34
or
LVMI > 149/122 (M/F) and RWT > 0.42
NTproBNP > 220/660 (SR/AF)
or
BNP > 80/240 (SR/AF)
*SR = sinus rhythm / AF = a.fib
MAJOR
MINOR
E/e’ (avg) 9-14,
or
TR vel > 2.8,
or
GLS < 16%
LAVI > 29-34,
or
LVMI > 115/95 (M/F), or RWT > 0.42,
or LVWT > 12 mm
NTproBNP > 115-220 or
BNP 35-80 in SR
or
NTproBNP > 365-660 or
BNP 105-240 in AF
MAJOR CRITERIA: 2 POINTS, MINOR CRITERIA: 1 POINT
HFA-PEFF score ≥ 5 points: HFpEF
HFA-PEFF score 2-4 points: diastolic stress test or invasive hemodynamics
HFA-PEFF score < 2 points: No HFpEF
Functional
Morphological
Biomarker

## Slide 15
H2FPEF score in MESA at Exam 6
Clinical variable | Score | Mean ± SD | 25th-75th %-tile | Prevalence
Heavy (BMI > 30 kg/m2) | 2 | 28.5±5.8 | 24.5-31.6 | 34%
Hypertensive (2 or more anti-HTN) | 1 | 1.3±1.4 | 0-2 | 37%
Atrial Fibrillation (AF on echo) | 3 | — | — | 3%
Pulmonary hypertension (Doppler PASP > 35 mmHg) | 1 | 33±8 | 28-37 | 23%
Elder (age > 60 years) | 1 | 74±9 | 67-81 | 99%
Filling pressures (E/e’ > 9) | 1 | 28.5±5.8 | 7.6-11.4 | 48%
Total H2FPEF Score | — | 2.7±1.4 | 0-9 | —

## Slide 16
H2FPEF score in MESA at Exam 6
Of N=3,254 with available data:
N=67 (2%) with pre-existing diagnosis of HF
N=17 (0.5%) with EF<40% on Exam 6 echo
N=320/3170 (10.1%) with H2FPEF Score 5+: > 80% probability of HFpEF

## Slide 17
Early HFpEF: QOL, exercise capacity
KCCQ-12 summary score
6MWT distance
Mean -8.3 point difference
P=2.5x10-25
Mean -65 m difference
P=2.4x10-22

## Slide 18
Early HFpEF: cardiac structure/fxn
LV mass index
LV ejection fraction
LV longitudinal strain
Mean +6 g/m2 difference
P=0.00002
Mean -0.29% difference
P=0.30
Mean -0.6 %-unit difference
P=0.0007

## Slide 19
Early HFpEF: cardiac structure/fxn
LA volume index
LA reservoir strain
Mean +6.4 ml difference
P=3.5x10-32
Mean -4.7%-unit difference
P=8.5x10-40

## Slide 20
CONDUIT
BOOSTER
LA strain

## Slide 21
LA strain: baseline vs. HF

## Slide 22
LA strain: A marker of LA fibrosis

## Slide 23
Abnormal LA mechanics in HFpEF
LA strain is a better predictor of outcomes compared to
LV or RV longitudinal strain
Freed B…Shah SJ. Circ CV Imaging 2016

## Slide 24
Abnormal LA mechanics in HFpEF
LA strain is a key determinant of exercise capacity in HFpEF
Freed B…Shah SJ. Circ CV Imaging 2016

## Slide 25
Abnormal LA mechanics in HFpEF
EXERCISE INTOLERANCE
ADVERSE OUTCOMES

## Slide 26
LA reservoir strain & submax VO2
LA reservoir strain is the most closely associated echo variable with CPET submax VO2 (n=126)
Association remains significant after adjustment for age, sex, BMI, a-fib
(Beta-coefficient = -0.6 ml/kg/min for each 1-SD decrease in LA reservoir strain, P<0.0001)
R=0.34
P<0.0001

## Slide 27
InterAtrial Shunt Device
8 mm
Feldman T…Shah SJ. Circ Heart Fail 2016
IASD proposed mode of action: dynamic decompression of
overloaded LA chamber by shunting blood from LA  RA

## Slide 28
Example patient randomized to IASD
Subcostal view (zoomed)
Subcostal view
LA
RA
LV
RV
12-month echo

## Slide 29
REDUCE LAP-HF I RCT
Feldman T… Shah SJ. Circulation 2018

## Slide 30
REDUCE LAP-HF I RCT: 1-yr. outcome
Shah SJ, et al. JAMA Cardiol 2018

## Slide 31
Validation of MESA Early HF diagnosis
Cardiopulmonary exercise testing:
n=135 complete at Wake Forest (treadmill)
Goal to do additional CPEX exams in MESA participants (n=150 at the Chicago field center (semi-recumbent bike + echo + wearables)

## Slide 32
Validation of MESA Early HF diagnosis
Peak VO2 is insufficient to make early HFpEF diagnosis in “grey zone”
Reddy Y…Borlaug B. JACC Heart Fail 2018

## Slide 33
Validation of MESA Early HF diagnosis
Diastolic stress echo to augment early HFpEF diagnosis
Peak VO2 is insufficient to make early HFpEF diagnosis in “grey zone”
Reddy Y…Borlaug B. JACC Heart Fail 2018

## Slide 34
Rest
25W exercise
E=72 cm/s
e’ = 4 cm/s
E = 154 cm/s
e’ = 7 cm/s
a'
a'
E/e’ = 18
E/e’ = 22
72-year-old woman with HFpEF

## Slide 35
72-year-old woman with HFpEF
Rest
25W
Exercise
LA reservoir
LA booster

## Slide 36
Microsoft Aurora wristwatch device
Continuous radial tonometry + accelerometer + HR monitor + position monitor

## Slide 37
RESTING ARTERIAL TONOMETRY
Pulse pressure = 117 AU

## Slide 38
15W (PEAK STRESS) ARTERIAL TONOMETRY
Pulse pressure = 98 AU

## Slide 39
Exercise sweat analytics
Choi J, et al.
Science Advances 2018

## Slide 40
Exercise sweat analytics
Choi J, et al.
Science Advances 2018

## Slide 41
PhysIQ vital patch + Samsung watch

## Slide 42: thank you
Shah Lab