## Slide 1: MESA – CT REPORT
Matthew Budoff
Budoff@ucla.edu

## Slide 2: MESA CT Changes
New Field of View (32 cm) – less incidental findings and lower radiation (40% reduction)
New Triggering (70-75% of the RR) – less motion artifacts
New Equipment – Toshiba 320 (Hopkins)
  Progression evaluation underway (C. Johnson)
Single Scan protocol

## Slide 3: Scientific Changes for Exam 5
We are obtaining thin slices (0.625-1.25 mm slices) in addition to normal 2.5-3 mm slices
  Should allow more visualization of CAC and more accurate quantification
E. Brown is evaluating a new scoring algorithm to capture calcification better

## Slide 4
WFU | GE 64 | Prior to 2002 - Lightspeed Qxi (4slice)
Columbia | Sensation 64 | Prior to 2005 - Imatron
Hopkins | Toshiba 320 | < 2004 - Siemens Volume Zoom
 |  | 11/2004 - 2/2005 Toshiba32
 |  | 2/2005 - 9/2007 Toshiba64
UMN | Sensation 16 | < 8/2004 - Siemens Volume Zoom
Chicago | GE 64 | Imatron
UCLA | Siemens Sensation64 | Imatron

## Slide 5
Proposed Study | Type of CT proposed | Participant/Sample | Cohort Overlap | Total Radiation Estimate | Total Time Estimate
MESA Air | 1 coronary CT scan using the MESA Exam 3/4 protocol | ~3,600: ~3,350 MESA ppt. + ~250 Air New Recruits | N/A | 1.4 mSv (women); 1.2 mSv (men) | 20 minute scanning + 20 min for check-in, check-out, & scheduling.
MESA Air | Aortic CT | ~2,138: ~1,888 MESA ppt + ~250 Air New Recruits | All ~ 2,138 ppt. will also receive an Air CAC scan | 2-3 mSv | 10 minutes if added to CAC scan
Cardiopulmonary interactions in MESA (MESA-Lung II) | 1 full-lung CT scan | 2,400 MESA Air/Lung participants + 650 MESA-Lung ppt not in Air; | Overlaps with 2,400 MESA Air CAC CT scan ppt. | 4.4 mSv (women); 2.8 mSv (men) | 1 min if performed at same time as CAC scan; 20 min for those not getting a CAC scan
MESA CTA | CT angiography | 600 MESA Participants with stable heart rates and normal GFR | Overlaps with MESA Air CAC CT scan | 3-5 mSv | 1 hour
(MESA Toe) | AP and lateral plain x-rays of the ankles | ~2200 participants | TBD | 0.1-0.3 mSv | 10 minutes
Note: Background radiation estimated as 3-5 mSv per year |  |  |  |  | 

## Slide 6: Progress to Date
        Number of Scans Done
3-WFU 71
4-Columbia 42
5-JHU 49
6-FairviewMN 86
7-NWU 75
8-UCLA 50
Grand Total 373
We are currently 2 weeks behind on reading.

## Slide 7: Radiation Doses
327 participants underwent calcium scoring. (LIMITS 3 mSev, DLP 214)
Median Dose mSev (DLP): 0.91 (65)
Maximum Dose mSev (DLP): 2.04 (146)
Minimum Dose mSev (DLP): 0.4 (29)
331 underwent lung Scanning: (LIMITS 6.5 mSev, DLP 470)
Median Dose mSev (DLP): 3.93 (281)
Maximum Dose mSev (DLP): 6.83 (488)
Minimum Dose mSev (DLP): 2.8 (200)
290 underwent both lung and CAC Scanning
Median Dose mSev (DLP): 4.91 (351) (LIMITS 9.5 mSev, DLP 684)
Maximum Dose mSev (DLP): 7.96 (569)
Minimum Dose mSev (DLP): 3.30 (236)

## Slide 8: Protocol Violations
Two types of Violations –
  5 participants received CAC scans that shouldn’t
6 protocol violations reported to PIs and CC (wrong body weight used):
  FairviewMN 2
  Columbia 4
Total: 6
These violations affected rad dose, but DLPs are still within IRB limits.
There were other minor deviations, e.g., Field of View, rotation time, recon kernel but these were not reported to PIs

## Slide 9: Additional Variables that have been obtained from calcium scan
Aortic valve, mitral valve, thoracic calcification - done
Left Ventricular size - done
Thoracic Aortic diameters - NEW
Pulmonary artery diameters - pending
Atrial sizes – done, J Carr
Bone density (thoracic) - pending
Pericardial fat – done, J Carr
Non-Alcoholic Fatty Liver Disease - NEW

## Slide 10: MESA CTA
Doing a multi-center, multi-vendor NIH study (W. Post – MACS CTA) - we have achieved doses of: 2.4±1 mSv
Endpoints Derived:
  Plaque composition (non-calcified, mixed, calcified)
  Plaque Score/quantity
  Stenosis Severity Score
  LV Mass/Hypertrophy
  LV Volume
  Left Atrial Volume
  Pericardial fat
  Coronary calcium
  Aortic valve calcification
  Mitral Annular calcification
  Thoracic calcification
  Infarction/Scar

## Slide 11: Multi-Ethnic Study of ATHEROSCLEROSIS